## Slide 1: HoloCam: Low-power wide-field incoherent target detector
Prasanna Pavani, Jonathan Hull, Sergey Chemishkian, Kathrin Berkner, Ken Gudan
6/24/2012
Notes: My name is Prasanna Pavani. I am with Ricoh Innovations in Menlo Park CA. In this talk, I will be introducing HoloCam, which is a target detector that exploits a new sensing paradigm that we call distribution sensitivity to achieve low-power and high-speed operation
Todo:
1. Verify 50cm range

## Slide 2: Low-power target detection
Detect target presence/absence with
  Low power (µW)
  High speed (KHz)
  Wide field (50˚)
  Compact size (cm3)
  Room light
Applications
  Automotive, Factory Automation, Consumer Electronics
Is target present?
No
Yes
Low-power target detector
Action
Target
Notes: Our goal is to design a target detector that generates a binary output to indicate the presence or absence of a target. And we’d like the target detector to consume very power, in the order of uW, operate at high speeds (at least khz),
Need for constant monitoring - Always on (sergey)

## Slide 3: Low-power target detection: Digital Processing
Detect target presence/absence with
  Low power (µW)
  High speed (KHz)
  Wide field (50˚)
  Compact size (cm3)
  Room light
Applications
  Automotive, Factory Automation, Consumer Electronics
Is target present?
No
Yes
Camera
Image Processing
Action
Target
Digital Processing: High power (mW), Low speed (30Hz)
J. A. Ratches, Opt. Eng. 50 (2011)
Notes: Camera + image processing consumes power
Optical correlator: laser, alignment sensitive, needs image processing

## Slide 4: Low-power target detection: Optical Correlator
Detect target presence/absence with
  Low power (µW)
  High speed (KHz)
  Wide field (50˚)
  Compact size (cm3)
  Room light
Applications
  Automotive, Factory Automation, Consumer Electronics
Optical
Correlator
Is target present?
No
Yes
Action
Target
Optical Correlator: Bulky, Alignment sensitive, Lasers
J. D. Armitage et al., Appl. Optics 4, 461 (1965)
Avi Pe’er et al., Optics Letters 24, 1469 (1999)
Pierre Ambs, Adv. in Opt. Tech., 372652 (2010)
Notes: Camera + image processing consumes power
Optical correlator: laser, alignment sensitive, needs image processing

## Slide 5: HoloCam: Low-power target detector
Target Hologram
  Encodes target features
  Single-element optical processing
Distribution Sensitive Detector
  Single-pixel spot/blur classifier
  Local-currents in non-uniform illumination
Features
  Low power (<20µW)
  High speed (2.5KHz)
  Wide field, Compact, Room light
Target
Hologram
Distribution Sensitive Detector (DSD)
Ambient-light Detector
Target
Notes: Talk about Ambient Light Detector (for normalizing illumination variations)

## Slide 6: Target Hologram Design
Computer Generated Hologram Optimization
  Wavefront control: projections on to convex sets
    Piestun et al., Opt. Lett. 19, 771 (1994)
  Initial Estimate: Matched Filter
  Hologram plane constraint: Phase-only
  Detector plane constraint: Confine intensity to tight spot
Detector Constraint
Spot size (w)
Quality (L) Estimator
Efficient Design
Yes
No
Maximum L
?
Initial Estimate
Target Hologram
Target Hologram Constraint (H)
Target
Hologram
Detector
Target

## Slide 7: Distribution Sensitive Detector
Target
Response
Single pixel spot/blur classifier
  Low current for “spot” response
  High current for “blur” response
Distribution Sensitivity
  Sensitive to optical intensity distribution
  Sensitive to optical power
  Non-uniform distribution increases losses
    Increased local currents
    Homogenizers in Concentrated Photovoltaics
Non-target
Response
Blur
DSD
High current
DSD
Spot
Low current
DSD
DSD
Notes: Emphasize one current value at a given time

## Slide 8: Target Detection: Wide Field of View
Transverse space invariance
  Hologram response moves on detector
  1cm3 device has ~50˚ field of view
Axial space variance
  Change in scale and defocus
  Operation range (
Multiplexed holograms
  For scale and rotation invariance
  For multiple targets
*k = (s: target size, f: focal length, : scale change)
Target
Hologram
Distribution Sensitive Detector (DSD)
Ambient-light Detector
Target
Operation
Range (𝛿𝑧)

## Slide 9: Results: Single Element Optical Processing
Spatial Light
Modulator (SLM)
Distribution Sensitive
Detector (DSD)
2D imager
Target
Target Hologram
Target Response
Non-target Response
DSD
230.7±11.7mV
DSD
472.9±11.5mV
Notes: Lens TH

## Slide 10: Results: Distribution Sensitive Detector
Chart: Time (s)
Fluorescent lamp flicker
Chart: 
| 0.63500000000000001 | 1.27 | 2.54 | 3.81 | 5.08 | 6.35 | 7.62 | 8.89
 | 0.1049 | 0.1588 | 0.304 | 0.459 | 0.634 | 0.88 | 1.1 | 1.297
Source distance (cm)
DSD output (Volts)
Load: 4KΩ

## Slide 11: QR Code Detection (simulation)
QR code targets have c values between 0 - 0.15
Fisher linear discriminant based classification
Detection model:
(Normalized voltage response)
Counts

## Slide 12: Conclusion
HoloCam: new target detector
  Target Hologram
  Distribution Sensitive Detector
  Low-power and high speed
Distribution Sensitive Detection is a new sensing paradigm
Single element optical processing allows for compact systems
Target
Hologram
Distribution Sensitive Detector (DSD)
Ambient-light Detector
Target
Notes: - Emphasize constant monitoring after first bullet (Always on) detector